## Slide 1
Project Presentation
IoT-Based Smart Medicine Box

## Slide 2
The Smart Medicine Box is an IoT-based healthcare solution that helps prevent missed or forgotten medications. Powered by an ESP32 and integrated with the Blynk app, it automatically opens scheduled compartments, triggers alarms, and sends real-time alerts to caregivers. IR sensors confirm whether the dose is taken, while a DHT11 sensor monitors storage conditions to keep medicines safe. This system enhances medication adherence and provides greater peace of mind for patients and families.
Introduction

## Slide 3
Our Team
Rabia
Laiba
Malika

## Slide 4
Project Goals
Automated Alerts: Sound and visual cues at specific times.
Environmental Monitoring: Tracking storage conditions (Temp/Humidity).
IoT Monitoring: Remote tracking of medication via a smartphone app.
Compliance Verification: Using IR sensors to confirm if the medicine was actually taken
Safety: Automatic locking/closing of compartments if a dose is missed.

## Slide 5
Problems
Forgetfulness in taking medication (especially for the elderly or those with chronic illnesses).
The Issue
Reduced treatment effectiveness, health complications, and hospital readmissions.
Consequences

## Slide 6
Software & Logic Flow
Initialization: Connects to Wi-Fi and Blynk; sets servo positions to "Closed."
The Alert Cycle: 1. Pre-set timer triggers. 2. Buzzer/LED turns ON + App notification sent. 3. Servo opens the specific compartment.
Confirmation Logic:
Success: IR Sensor detects movement → System resets → App updated.
Missed Dose: 60-second timeout → Lid closes → "Missed Dose" alert
1
2
3

## Slide 7
IOT Integration
Real-time Dashboard: View Temperature and Humidity graphs.
1
Remote Control: A "Silence" button (V1) to stop the buzzer manually.
Live Status: Indicators for each IR sensor (V10-V12).
2
Events: Push notifications for "Medicine Time" and "Missed Dose."

## Slide 8
Hardware Components
ESP32: Main controller with built-in Wi-Fi.
Servos (MG90S): Mechanically opens/closes 3 separate compartments.
IR Sensors: Detects hand movement to verify medicine retrieval.
DHT11: Monitors if pills are stored in safe temperature/humidity.

## Slide 9
Advantages & Future Scope
  Reduces human error.
  Allows caregivers to monitor patients remotely.
  Compact and low power consumption.
Advantages
  Integration with Google Assistant for voice reminders.
  Face recognition to ensure the correct person takes the pill.
  Reorder system that texts the pharmacy when pills are low.
Future Scope

## Slide 10
Conclusion
The Smart Medicine Box is a life-saving tool that bridges the gap between healthcare and IoT.

## Slide 11
Q&A Session

## Slide 12
Thank You